Notes on splines:
- Calculates a temp matrix
- Four control points p0,p1,p2,p3 (travel segment is between p1->p2)
- Four coefficients (also vec 3) = ctrl points * weight matrix
- Iterative attempts (max 8) to attempt to fit within the corridor tetragon
  - Each attempt either reports success or alters one point on the curve that is outside the tetragon, and alters the curve so that point is within
- tau is tension parameter, tightness to the chord
- bias is parameter for anticipation vs. overshoot, for cusps
- gamma is a parameter for curvature (don’t really use it much)
- Standard coefficients:
  - a = 0.5f * (1.0f - tau0) * (1.0f + bias0) /* * (1.0f + gamma0 the continuity param)*/
  - b = 0.5f * (1.0f - tau0) * (1.0f - bias0) /* * (1.0f - gamma0 the continuity param)*/
  - c = 0.5f * (1.0f - tau1) * (1.0f + bias1) /* * (1.0f - gamma1 the continuity param)*/
  - d = 0.5f * (1.0f - tau1) * (1.0f - bias1) /* * (1.0f + gamma1 the continuity param)*/
- Computed weight matrix is the precomputed
  - based on the specifics of tau and bias of the end points of the travel segment
  - based on the chord length of the three segments
  - Uses the standard a,b,c,d weight bases
  - not much to it m00 = (a*d1*d1)/((d0*d0)+(d0*d1)) sort of thing
- returned coef vector is the weight matrix multiplied by the control points (as stated above)
  - Impl is just to multiply out the rows of the matrix as a the weights for a linear weighted sum of the points
- Fit to corridor task does a couple of things.
  - Rotates the corridor and control points into a “standard” alignment axis (z in example) aligned on the chord of the travel segment
    - For the record, this is as simple as
      - atan2 to get the angle of (say x, and z components of the travel chord)
      - then get the cos/sin for the this angle
      - normalize all points (so travel segment starts at origin) and rotate out the points
  - I would love to avoid these rotations, as the feel unnecessary, but it will take a bunch more math to figure that out
    - TODO
  - Compute the undulation points to find current extremes (which are our only possibilities for exceeding the tetragon bounds)
    - This is valid for a quadratic curve, but not quartic or quintic or above
    - Some simplifying assumptions let us treat this as just solving the quadratic roots of the derivative
      - Curve derivative (based on coef)
        - 3A(t^2) + 2Bt + C
        - Since we multiply coefs (a,b,c,d) by a time vector (with the powers of time) we can just multiply our coef (and drop the D) to get the tangent (and similar for higher derivatives)
      - Since we’re coaxial (z) just take the orthogonal component (in this case coef.x) of the tangent coefs
      - Solve the quadratic roots
      - These roots are the times for the extremes of the curve, test them for extreme points of the curve
      - Get these points and test them against the tetragon
  - If a point is outside of the tetragon
    - Figure out where the farthest point should be (the wall of the tetragon in this case)
    - Call this adjusted point P4 (or whatever is more meaningful)
    - Since we’re coaxial (z) again we can use the simplifying assumption that our points (p0,p1,2p3… p4) are just the orthogonal (x) component
      - Meaning we don’t need to expand the limit (p4) to a real point, it’s just however far off the chord we want the curve to go instead of the prev undulation point
    - if the adjustment point (p4) is in the first half of the travel segment then we’re using it (and the tau/bias for p2, the end of the travel segment) to solve for a new tau0 (tau of p1 the first point of the travel segment)
    - Otherwise solve for a new tau1 ( tau of p2, the end of the travel segment) using the tau/bias from p1
    - Be sure that the denominators are not 0 and that tau is clamped to -1..1
  - Later on, may want to consider solving for bias and gamma too
- Position is just weighted linear sum of coefs by powers of time
  - Pos(t) = a(t^3) + b(t^2) + ct + d
  - This could be a vector mult if you’ve got a nice simd vector/mat op